## Slide 1: W3C Web of Things Plugfest Security Review
Michael McCool
W3C WoT WG Security and Privacy TF
Bundang, July 2018

## Slide 2: Outline
Who tried what
  Intel, Panasonic, Smart Things, Siemens, EURECOM, others?
  HTTPS (direct and via proxy), Auth (basic, digest, bearer tokens, psk)
Issues Arising
  Security Metadata Structure
    Definitions, multiple levels (2? 3?)
  Security Metadata Content
    Schemes, scheme parameters, vocabulary
  Interactions with Architecture
    Proxies
TO DO
  Online and plugfest
  Security testing and validation

## Slide 3: Intel
Auth
  HTTP Basic
  HTTP Digest
Encryption
  HTTPS Proxy endpoint, Let's Encrypt certs
    Running in cloud service
    Transparent proxy (endpoint wrapper)
    Both cloud and reverse tunneled HTTP services
  Direct HTTPS with Let's Encrypt certs
    Running on local device; reverse tunneled out and exposed on cloud endpoint
    Certificate valid for cloud endpoint; but TLS managed by device (end-to-end security)
  Direct HTTPS with self-signed certs
    For local devices
    Client must accept self-signed cert
Secured services
  Thing Directories (cloud and gateway)
  Thing Playground (cloud)
  OCF-WoT metadata bridge (gateway)
  CoAP/HTTP bridge (gateway)
  OCF devices (via CoAP/HTTP bridge)
  Simple-webcam (native web service)
Other notes
  Two cloud servers
  Two separate local networks behind NATs
  TDs with multiple forms (different endpoints) with different security for the same physical device
  Challenges with port 22 being blocked…

## Slide 4: Siemens
Auth
  HTTP basic
  JWT bearer tokens
Encryption
  HTTPS
Other
  HTTP proxy support:
    Both forward proxies and reverse proxies (things only reachable through proxies)
  Used with Oracle instance
  Bearer tokens with Fujitsu beacon light

## Slide 5: Panasonic: Implementation 1
Bearer authentication using "bearer" security scheme
  Indicated authorization Url…
  But actually formed a bearer token manually
Specified security in TD by default
Indicated no authentication is required using "security": [] override.
At top level, used this:
"security": [{
"scheme": "bearer",
"format": "jwt",
"alg": "ES256",
"authorizationUrl": "…"
}],
In forms for interactions that did not use security, used this:
"forms": [
{"href": "operationStatus",
"mediaType": "application/json"},
{"href": "https://…/operationStatus",
"mediaType": "application/json",
"subProtocol": "LongPoll",
"rel": "observeProperty",
"security": []
},
{"href": "wss://…./operationStatus",
"mediaType": "application/json",
"rel": "observeProperty",
"security": []
}
]

## Slide 6: Panasonic: Implementation 2
Online WoT Server Simulator requires the following HTTP header upon request
X-PWOT-TOKEN: <access token>
However, the TD is not correct at this moment. Currently we have:
"security": [{
"cat": "token:jwt",
"alg": "ES256",
"as": "https://plugfest.thingweb.io:8443"
}],
It should updated to the new TD specs.
It should use "scheme": "apikey".
==> plan to update the TD of Online WoT Server Simulator by the next PlugFest.

## Slide 7: Smart Things
Example TDs for CoAP devices using PSK
Raising need for CoAP-specific security metadata
MQTT metadata can probably reuse existing vocabulary, eg "basic"
  An assumption that needs to be tested

## Slide 8: Eurecom
Auth:
  Bearer tokens
Encryption
  HTTPS for both Things and TD service
  TDs encrypted and decrypted after download using pre-shared key

## Slide 9: Issues Arising
NAT Traversal
  Can't depend on port 22 being open…
Pre-shared keys
  Is "scheme": "psk" needed?
Self-signed certificates
  Need to validate certificate: Onboarding service? Validation service?
  Is "scheme": "cert" needed?
Security definitions vs activated security configurations
Multilevel security configurations
  Right now can be given at three levels; top, interaction, form
  Configurations at lower overrides higher
  All three needed?
"Add-on" security configurations
  Would be nice to have way to add configs, not just overrides

## Slide 10: Next
Implementations/use cases for all existing schemes
New schemes
  Local TLS/DTLS
  MQTT, CoAP, OCF
  Basic auth over HTTPS, Digest over (local) HTTP
Demonstration of at least one scheme using external vocabulary
  And maybe move some existing schemes out to external vocabulary…