## Slide 1: W3C Web of Things Security Metadata Proposal
Michael McCool
W3C WoT WG Security and Privacy TF
Prague, March 2018

## Slide 2: Outline
Issues
Goals and Requirements
Examples
For details…
  See https://github.com/w3c/wot-security/pull/86 for details
  Eventually will be merged into https://github.com/w3c/wot-security/blob/working/wot-security-metadata.md
  Longer term, should be merged into TD deliverable

## Slide 3: Issues
Many different security authorization schemes
Interactions may have multiple forms with different protocols
  And different protocols may support different security schemes
Different interactions may require different security configurations
  This can also be supported with separate Things, but this is awkward
  Fine-grained per-interaction control is useful to support roles, scopes (eg for OAuth), etc.
We would like to have overall defaults and local per-form overrides
  But this may or may not be easy to do with JSON-LD…

## Slide 4: Goals and Requirements
Support shared configurations
Support per-form security configuration
Support OR-AND combinations of schemes
Avoid redundancy
Avoid verbosity
Be as consistent as possible with related standards
  Such as OpenAPI, RAML, OCF, etc.
Support a range of security configurations used in practice
  But conversely, keep the scope narrow enough that attack surface is minimized and testing is practical
Describe, don’t prescribe…

## Slide 5: Examples
Basic Example
  Basic Authentication
  API Keys
  OCF Security
Additional Examples
  Bearer Tokens using JWT
  Proxies
  OAuth

## Slide 6: Basic Example
{
"@context": ["https://w3c.github.io/wot/w3c-wot-td-context.jsonld"],
"@type": ["Thing"],
"name": "MyLampThing",
"@id": "urn:dev:wot:my-lamp-thing",
"security": [
{
"@id": "basic-config",
"scheme": "basic"
},
{
"@id": "ocf-config",
"scheme": "ocf"
},
{
"@id": "apikey-config",
"scheme": "apikey",
"in": "header"
}
],
Basic Authentication Configuration
OCF Security Configuration
API Key Configuration

## Slide 7: Basic Example
"interaction": [
{
"@type": ["Property"],
"name": "status",
"schema": {"type": "string"},
"writable": true,
"observable": true,
"form": [
{
"href": "coaps://mylamp.example.com:5683/status",
"mediaType": "application/json",
"method": "coap:get",
"security": "ocf-config"
},
{
"href": "coaps://mylamp.example.com:5683/status",
"mediaType": "application/json",
"method": "coap:post",
"security": ["ocf-config","apikey-config"]
},
OCF Security
OCF Security + API Key
CoAPS
CoAPS

## Slide 8: Basic Example
{
"href": "https://mylamp.example.com/status",
"mediaType": "application/json",
"method": "http:get",
"security": "basic-config"
},
{
"href": "https://mylamp.example.com/status",
"mediaType": "application/json",
"method": "http:post",
"security": ["basic-config","apikey-config"]
},
]
},
Basic authentication AND API key
Basic authentication
HTTPS
HTTPS

## Slide 9: Basic Example
{
"@type": ["Action"],
"name": "toggle",
"form": [
{
"href": "coaps://mylamp.example.com:5683/toggle",
"mediaType": "application/json"
"security": ["ocf-config","apikey-config"]
},
{
"href": "https://mylamp.example.com/toggle",
"mediaType": "application/json"
"security": ["basic-config","apikey-config"]
}
]
},
OCF security AND API key
Basic authentication AND API key
CoAPS
HTTPS

## Slide 10: Basic Example
{
"@type": ["Event"],
"name": "overheating",
"schema": {"type": "string"},
"form": [
{
"href": "coaps://mylamp.example.com:5683/oh",
"mediaType": "application/json"
"security": "ocf-config"
},
{
"href": "https://mylamp.example.com/oh",
"mediaType": "application/json"
}
]
}
]
}
No security
OCF security
HTTPS
CoAPS

## Slide 11: Bearer Tokens
{
"@context": ["https://w3c.github.io/wot/w3c-wot-td-context.jsonld"],
"@type": ["Thing"],
"name": "FujitsuBeacon",
"@id": "urn:dev:wot:fujitsu-beacon",
"security": [
{
"@id": "bearer-token-config",
"scheme": "token",
"format": "jwt",
"alg": "ES256",
"as": "https://plugfest.thingweb.io:8443/"
},
... // other security configurations, if needed
],
...
Bearer Token Configuration

## Slide 12: Bearer Tokens
"interaction": [
{
"form": [
{
...
"security": "bearer-token-config"
},
... // other forms
},
... // other interactions
]
}
Bearer token authentication

## Slide 13: Proxies
{
"@context": ["https://w3c.github.io/wot/w3c-wot-td-context.jsonld"],
"@type": ["Thing"],
"name": "Festo",
"@id": "urn:dev:wot:festo",
"security": [
{
"@id": "proxy-config",
"scheme": "basic",
"proxy": "http://plugfest.thingweb.io:8087"
},
{
"@id": "endpoint-config",
... // details omitted; independent of proxy configuration
},
... // other security configurations, if needed
],
...
Proxy Security Configuration
Endpoint Security Configuration

## Slide 14: Proxies
"interaction": [
{
"form": [
{
...
"security": ["proxy-config","endpoint-config"]
},
... // other forms
},
... // other interactions
]
}
Combined Proxy and Endpoint Security

## Slide 15: OAuth
{
"@context": ["https://w3c.github.io/wot/w3c-wot-td-context.jsonld"],
"@type": ["Thing"],
"name": "Camera",
"@id": "urn:dev:wot:camera",
"security": [
{
"@id": "oauth-config",
"scheme": "oauth2",
"flow": "code",
"as": "https://example.com/api/oauth/dialog",
"ts": "https://example.com/api/oauth/token",
"rs": "https://example.com/api/oauth/refresh",
"scope": [
{ "name": "read:frame" },
... // other scopes
]
}
... // other security configurations, if needed
],
...
OAuth2 Security Configuration
OAuth2 “Code” Flow Configuration
OAuth2 Named Authentication Scopes

## Slide 16: OAuth
"interaction": [
{
"@type": ["Property"],
"name": "frame",
...
"writable": false,
"observable": true,
"form": [
{
"href": "https://example.com/api/frame",
"mediaType": "image/jpeg",
"method": "http:get",
"security": ["oauth-config"],
"auth": ["read:frame"]
},
... // other forms
},
... // other interactions
]
}
OAuth Security
OAuth Authorization Scopes

## Slide 17: Details
List of security schemes supported
Detailed definitions of tags
  https://github.com/w3c/wot-security/pull/86
  https://github.com/w3c/wot-security/blob/working/wot-security-metadata.md
To Discuss:
  Compatibility with JSON-LD
    Use of defaults, arrays, @id, etc.
  List of supported security mechanisms
  Validation issues
    There are only certain valid combinations of scheme and protocol…
  Bikeshed issues: names (“as” vs. “authenticationUrl”, etc.)